## Slide 1: CSE 140 Computer Architecture
Lecture 13 – Register Renaming

## Slide 2: Announcement
No new assignment this week
  Wrap up HW #3 and Project #1 in labs
Project #1
  Due 10/11 (Friday) at 11:59pm
Midterm #1
  10/17, during lecture (not 10/10)
  Lectures #1 - #8 (No virtual memory)
  HW #1 - #3
  Review on 10/15
Reading assignment
  Chapter 4.9, 4.10, 4.12
    Do all Participation Activities in each section
    Due Thursday (10/10) at 11:59pm

## Slide 3: Complex Pipelining: Motivation
Pipelining becomes complex when we want high performance in the presence of:
  Long latency or partially pipelined floating-point units
  Memory systems with variable access time
  Multiple arithmetic and memory units

## Slide 4: Complex Pipeline
IF
ID
WB
ALU
Mem
Fadd
Fmul
Fdiv
Issue
GPR’s
FPR’s
Can we solve write hazards without equalizing all pipeline depths and without bypassing?
Out-of-order execution!

## Slide 5: Out-of-order Completion
Latency
I1 DIV.D f6, f6, f4 4
I2 LD f2, 45(x3) 1
I3 MULT.D f0, f2, f4 3
I4 DIV.D f8, f6, f2 4
I5 SUB.D f10, f0, f6 1
I6 ADD.D f6, f8, f2 1
in-order comp 1 2
out-of-order comp 1 2
1 2 3 4 3 5 4 6 5 6
2 3 1 4 3 5 5 4 6 6
In-order Issue
Completion order has to follow instr. order
Completion order doesn’t need s to follow instr. order

## Slide 6: When is it Safe to Issue an Instruction?
Suppose a data structure keeps track of all the instructions in all the functional units
The following checks need to be made before the Issue stage can dispatch an instruction
  Is the required functional unit available?
  Is the input data available? → RAW?
  Is it safe to write the destination? → WAR? WAW?
  Is there a structural conflict at the WB stage?

## Slide 7: A Data Structure for Correct Issues
The instruction i at the Issue stage consults this table
  FU available? check the busy column
  RAW? search the dest column for i’s sources
  WAR? search the source columns for i’s destination
  WAW? search the dest column for i’s destination
    An entry is added to the table if no hazard is detected;
    An entry is removed from the table after Write-Back
Unit Name Busy Op Dest Src1 Src2
Int
  Mem
  Add1
  Add2
  Add3
  Mult1
  Mult2
  Div
Keeps track of the status of Functional Units

## Slide 8: Simplifying the Data Structure
Assuming In-order Issue
Suppose the instruction is not dispatched by the Issue stage if a RAW hazard exists or the required FU is busy, and that operands are latched by functional unit on issue:
  Can the dispatched instruction cause a
    WAR hazard?
      NO: Operands read at issue
    WAW hazard?
      YES: Out-of-order completion

## Slide 9: Simplifying the Data Structure
No WAR hazard
  no need to keep src1 and src2
The Issue stage does not dispatch an instruction in case of a WAW hazard
  a register name can occur at most once in the dest column
WP[reg#] : a bit-vector to record the registers for which writes are pending
  These bits are set by the Issue stage and cleared by the WB stage

## Slide 10: Scoreboard for In-order Issues
Busy[FU#] : a bit-vector to indicate FU’s availability.
        (FU = Int, Add, Mult, Div)
  These bits are hardwired to FU's.
WP[reg#] : a bit-vector to record the registers for which writes are pending.
  These bits are set by Issue stage and cleared by WB stage
Issue checks the instruction (opcode dest src1 src2)
against the scoreboard (Busy & WP) to dispatch
    FU available?
    RAW?
    WAR?
    WAW?
Busy[FU#]
WP[src1] or WP[src2]
cannot arise
WP[dest]

## Slide 11: Scoreboard Dynamics
I1 DIV.D f6, f6, f4
I2 LD f2, 45(x3)
I3 MULT.D f0, f2, f4
I4 DIV.D f8, f6, f2
I5 SUB.D f10, f0, f6
I6 ADD.D f6, f8, f2
  Functional Unit Status Registers Reserved
  Int(1) Add(1) Mult(3) Div(4) WB for Writes
t0 I1 f6 f6
t1 I2 f2 f6 f6, f2
t2 f6 f2 f6, f2 I2
t3 I3 f0 f6 f6, f0
t4 f0 f6 f6, f0 I1
t5 I4 f0 f8 f0, f8
t6 f8 f0 f0, f8 I3
t7 I5 f10 f8 f8, f10
t8 f8 f10 f8, f10 I5
t9 f8 f8 I4
t10 I6 f6 f6
t11 f6 f6 I6

## Slide 12: In-Order Issue Limitations
latency
1 LD f2, 34(x2) 1
2 LD f4, 45(x3) long
3 MULT.D f6, f4, f2 3
4 SUB.D f8, f2, f2 1
5 DIV.D f4, f2, f8 4
6 ADD.D f10, f6, f4 1
In-order: 1 (2,1) . . . . . . 2 3 4 4 3 5 . . . 5 6 6
1
2
3
4
5
6
In-order issue restriction prevents instruction 4 from being dispatched

## Slide 13: Out-of-Order Issue
Issue stage buffer holds multiple instructions waiting to issue.
Decode adds next instruction to buffer if there is space and the instruction does not cause a WAR or WAW hazard.
  Note: WAR possible again because issue is out-of-order (WAR not possible with in-order issue and latching of input operands at functional unit)
Any instruction in buffer whose RAW hazards are satisfied can be issued (for now at most one dispatch per cycle). On a write back (WB), new instructions may get enabled.
IF
ID
WB
ALU
Mem
Fadd
Fmul
Issue

## Slide 14: Issue Limitations: In-Order and Out-of-Order
latency
1 LD f2, 34(x2) 1
2 LD f4, 45(x3) long
3 MULT.D f6, f4, f2 3
4 SUB.D f8, f2, f2 1
5 DIV.D f4, f2, f8 4
6 ADD.D f10, f6, f4 1
In-order: 1 (2,1) . . . . . . 2 3 4 4 3 5 . . . 5 6 6
1
2
3
4
5
6
Out-of-order: 1 (2,1) 4 4 . . . . 2 3 . . 3 5 . . . 5 6 6
Out-of-order execution did not allow any significant improvement!
Antidependence
WAR

## Slide 15: How many instructions can be in the pipeline?
Which features of an ISA limit the number of
instructions in the pipeline?
Out-of-order dispatch by itself does not provide any significant performance improvement!
Number of Registers
Notes: Ilustrates how one feature alone may not help – happens today when people study single new idea in a very detailed model.

## Slide 16: Overcoming the Lack of Register Names
It was observed that … Floating Point pipelines often cannot be kept filled with small number of registers.
IBM 360 had only 4 floating-point registers (double)
Can a microarchitecture use more registers than
specified by the ISA without loss of ISA compatibility ?
    Robert Tomasulo of IBM suggested an ingenious solution in 1967 using on-the-fly Register Renaming
    (more physical registers than “architected” registers)

## Slide 17: Issue Limitations: In-Order and Out-of-Order
latency
1 LD f2, 34(x2) 1
2 LD f4, 45(x3) long
3 MULT.D f6, f4, f2 3
4 SUB.D f8, f2, f2 1
5 DIV.D f4’, f2, f8 4
6 ADD.D f10, f6, f4’ 1
1
2
3
4
5
6
Any antidependence can be eliminated by renaming.
    Compiler could be smarter about register use.
    Can it be done in hardware?
yes!
X
In-order: 1 (2,1) . . . . . . 2 3 4 4 3 5 . . . 5 6 6
Out-of-order: 1 (2,1) 4 4 5 . . . 2 (3,5) 3 6 6
WAR

## Slide 18: Register Renaming
Decode performs register renaming and adds instructions to the issue-stage instruction reorder buffer (ROB)
 renaming makes WAR or WAW hazards impossible
Why?
Any instruction in ROB whose RAW hazards have been satisfied can be dispatched.
 Out-of-order or dataflow execution (Dynamic pipeline scheduling)
IF
ID
WB
ALU
Mem
Fadd
Fmul
Issue

## Slide 19
Renaming Structures
Renaming
table &
regfile
Reorder
buffer
Load
Unit
FU
FU
Store
Unit
< t, result >
Ins# use exec op p1 src1 p2 src2
t1
t2
.
.
tn
Instruction template (i.e., tag t) is allocated by the Decode stage, which also associates tag with register in regfile
When an instruction completes, its tag is deallocated
Replacing the
tag by its value
is an expensive
operation

## Slide 20: Reorder Buffer Management
Instruction slot is candidate for execution when:
    It holds a valid instruction (“use” bit is set)
    It has not already started execution (“exec” bit is clear)
    Both operands are available (p1 and p2 are set)
t1
t2
.
.
.
tn
ptr2
next to
deallocate
ptr1
next
available
Ins# use exec op p1 src1 p2 src2
Destination registers are renamed to the instruction’s slot tag
ROB managed circularly
  “exec” bit is set when instruction begins execution
  When an instruction completes its “use” bit is marked free
  ptr2 is incremented only if the “use” bit is marked free

## Slide 21: Renaming & Out-of-order Issue An example
When are tags in sources
replaced by data?
When can a name be reused?
1 LD f2, 34(x2)
2 LD f4, 45(x3)
3 MULT.D f6, f4, f2
4 SUB.D f8, f2, f2
5 DIV.D f4, f2, f8
6 ADD.D f10, f6, f4
Renaming table
Reorder buffer
Ins# use exec op p1 src1 p2 src2
t1
t2
t3
t4
t5
.
.
data / ti
p data
f1
f2
f3
f4
f5
f6
f7
f8
Whenever an FU produces data
Whenever an instruction completes
t1
1 1 0 LD
t2
2 1 0 LD
5 1 0 DIV 1 v1 0 t4
4 1 0 SUB 1 v1 1 v1
t4
3 1 0 MUL 0 t2 1 v1
t3
t5
v1
1 1 1 LD
0
4 1 1 SUB 1 v1 1 v1
4 0
v4
5 1 0 DIV 1 v1 1 v4
2 1 1 LD
2 0
3 1 0 MUL 1 v2 1 v1

## Slide 22: IBM 360/91 Floating-Point Unit R. M. Tomasulo, 1967
Mult
1
1
2
3
4
5
6
load
buffers
(from
memory)
1
2
3
4
Adder
1
2
3
Floating-Point
Regfile
store buffers
(to memory)
...
instructions
Common bus ensures that data is made available immediately to all the instructions waiting for it.
Match tag, if equal, copy value & set presence “p”.
Distribute
instruction
templates
by
functional
units
< tag, result >
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
2
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data

## Slide 23: Effectiveness?
Renaming and Out-of-order execution was first
implemented in 1969 in IBM 360/91 but did not show up in the subsequent models until mid-Nineties.
Why ?
Reasons
    1. Effective on a very small class of programs
    2. Memory latency a much bigger problem
    3. Exceptions not precise!
    One more problem needed to be solved
Control transfers (branch)

## Slide 24: Precise Interrupts
It must appear as if an interrupt is taken between two instructions (say Ii and Ii+1)
  the effect of all instructions up to and including Ii is totally complete
  no effect of any instruction after Ii has taken place
The interrupt handler either aborts the program or
restarts it at Ii+1 .

## Slide 25: Effect on Interrupts Out-of-order Completion
I1 DIV.D f6, f6, f4
I2 LD f2, 45(r3)
I3 MULT.D f0, f2, f4
I4 DIV.D f8, f6, f2
I5 SUB.D f10, f0, f6
I6 ADD.D f6, f8, f2
out-of-order comp 1 2 2 3 1 4 3 5 5 4 6 6
Consider interrupts
Precise interrupts are difficult to implement at high speed
- want to start execution of later instructions before
exception checks finished on earlier instructions
restore f2
restore f10

## Slide 26: Exception Handling (In-Order Five-Stage Pipeline)
Hold exception flags in pipeline until commit point (M stage)
Exceptions in earlier pipe stages override later exceptions
Inject external interrupts at commit point (override others)
If exception at commit: update Cause and EPC registers, kill
all stages, inject handler PC into fetch stage
Asynchronous Interrupts
Exc
D
PC
D
PC
Inst. Mem
D
Decode
E
M
Data Mem
W
+
Exc
E
PC
E
Exc
M
PC
M
Cause
EPC
Kill ID Stage
Kill IF Stage
Kill EXE Stage
Illegal Opcode
Overflow
Data Addr Except
PC Address Exceptions
Kill Writeback
Select Handler PC
Commit Point

## Slide 27: Phases of Instruction Execution
Fetch: Instruction bits retrieved from cache.
I-cache
Fetch Buffer
Issue Buffer
Functional Units
Architectural
State
Execute: Instructions and operands issued to execution units.
When execution completes, all results and exception flags are available.
Decode: Instructions dispatched to appropriate issue-stage buffer
Result Buffer
Commit: Instruction irrevocably updates architectural state (aka “graduation”).
PC
Commit
Decode/Rename

## Slide 28: In-Order Commit for Precise Exceptions
Instructions fetched and decoded into instruction
reorder buffer in-order
Execution is out-of-order (  out-of-order completion)
Commit (write-back to architectural state, i.e., regfile &
memory, is in-order
Temporary storage needed to hold results before commit (shadow registers and store buffers)
Fetch
Decode
Execute
Commit
Reorder Buffer
In-order
In-order
Out-of-order
Exception?
Kill
Kill
Kill
Inject handler PC

## Slide 29: Extensions for Precise Exceptions
Reorder buffer
ptr2
next to
commit
ptr1
next
available
add <pd, dest, data, cause> fields in the instruction template
commit instructions to reg file and memory in program
order  buffers can be maintained circularly
on exception, clear reorder buffer by resetting ptr1=ptr2
(stores must wait for commit before updating memory)
Inst# use exec op p1 src1 p2 src2 pd dest data cause

## Slide 30: Rollback and Renaming
Register file does not contain renaming tags any more.
How does the decode stage find the tag of a source register?
Search the “dest” field in the reorder buffer
Register File
(now holds only committed state)
Reorder
buffer
Load
Unit
FU
FU
FU
Store
Unit
< t, result >
t1
t2
.
.
tn
Ins# use exec op p1 src1 p2 src2 pd dest data
Commit

## Slide 31: Renaming Table
Register File
Reorder
buffer
Load
Unit
FU
FU
FU
Store
Unit
< t, result >
t1
t2
.
.
tn
Ins# use exec op p1 src1 p2 src2 pd dest data
Commit
Rename
Table
Renaming table is a cache to speed up register name look up. It needs to be cleared after each exception taken.
When else are valid bits cleared?
Control transfers (branches)
r1
t
v
r2
tag
valid bit